## Slide 1: Computer Organization and Assembly Language
Lecture 2

## Slide 2: This lecture will cover
Instruction Execution Cycle
Instruction Set/Groups (1.3 BH)
Basic operand Type
INTEL IAPX88 ARCHITECTURE (1.5 BH)
  Registers (1.2, 1.6 BH)
  Buses and Memory
First program in Assembly (1.7 BH)
  Introduction to DosBox, NASM, AFD

## Slide 3: Instruction Execute Cycle
Obtain instruction from program storage
Determine required actions and instruction size
Locate and obtain operand data
Compute result value and status
Deposit results in storage for later use
Instruction
Decode
Instruction
Fetch
Operand
Fetch
Execute
Writeback
Result
Infinite Cycle

## Slide 4: Instruction Execution Cycle – cont'd
Instruction Fetch
Instruction Decode
Operand Fetch
Execute
Result Write back
I2
I3
I4
PC
program
I1
instruction
queue
op1
op2
memory
fetch
ALU
registers
write
decode
execute
read
write
(output)
registers
flags
. . .
I1
Notes: These concepts will be used in pipelining…..

## Slide 5: Instruction Group
Data Movement Instructions
  These instructions are used to move data from one place to another.
  These places can be registers, memory, or even inside peripheral devices. Some examples are:
    mov ax, bx
    lad 1234
Arithmetic and Logic Instructions
  Arithmetic instructions like addition, subtraction, multiplication, division and Logical instructions like logical and, logical or, logical xor, or complement are part of this group.
  Some examples are:
    and ax, 1234
    add bx, 0534
    add bx, [1200]

## Slide 6: Instruction Group
Program Control Instructions
  These are instructions that control the program execution and flow by playing with the instruction pointer and altering its normal behavior to point to the next instruction.
  Some examples are:
  cmp ax, 0
  jne 1234
Special Instructions
  Another group called special instructions works like the special service commandos. They allow changing specific processor behaviors and are used to play with it. They are used rarely but are certainly used in any meaningful program. Some examples are:
    cli
    sti
  Where cli clears the interrupt flag and sti sets it

## Slide 7: BASIC OPERAND TYPES
Registers
  Uses a named register in the CPU
  Example
    mov si,cx
    add ax,bx
Immediate operands
  Constant expressions such as number , character constants or symbols are immediate operands, for example
    mov ax,10
    add ax,5

## Slide 8: BASIC OPERAND TYPES
Direct operands
  Refers to the content of memory at a location identified by a label in data segment, for example
    mov ax, [num1]
    num1: dw 5
Direct offset operand
  Refers to the content of memory at a location identified by a label in data segment by +/- a value from offset, for example
    mov ax, [num1+1]
    num1: dw 5
    dw 10
*Note that declaring data will be covered in coming lectures

## Slide 9: INTEL IAPX88 ARCHITECTURE

## Slide 10: Registers
Types of Registers
  Accumulator
    Central register in every processor
    Traditionally all mathematical and logical operations are performed on the accumulator
    n bit processor has n bit accumulator. For example a 16 bit processor has 16 nit accumulator.
  Pointer, Index, or Base Register
    Holds the address of data
  Flag Register
    This is a special register in every architecture called the flags register or the program status word.
    The bits of the flags register work independently and individually, and combined its value is meaningless.
    An example of a bit commonly present in the flags register is the carry flag
    If a 16bit number is added to a 16bit accumulator, and the result is of 17 bits the 17th bit is placed in the carry bit of the flags register.
  Program Counter or Instruction Pointer
    The program counter holds the address of the next instruction to be executed

## Slide 11: IAPX88 REGISTER ARCHITECTURE
8088 is a 16bit processor with its accumulator and all registers of 16 bits
Consists of 14 registers.
General Registers
Index Registers
Instruction Pointer
Stack Pointer
Base Pointer
Flags Register
Segment Registers

## Slide 12: General Registers (AX, BX, CX, and DX)
Used for arithmetic and data movement
X in their names stand for extended meaning 16bit registers
  For example AX means we are referring to the extended 16bit “A” register
Upper and lower half can be accessed separately,
  For example
    AH is for upper 8 bits (A high byte)
    AL for lower 8 bits (A low byte)
    AX is used to access whole 16 bits
  Any changes in AH or AL are reflected in AX.

## Slide 13: General Registers (AX, BX, CX, and DX)
AX, A for accumulator, is the accumulator register as it is favored by CPU for arithmetic operations. Provides slightly more efficiency.
BX, B for base, register can hold the address or procedure or variable. BS can also perform arithmetic or data movement.
CX, C for counter, acts as counter for repeating or loop instructions. These instructions automatically repeat and decrement CX.
DX (D for data), has special role in multiply and divide operations, When multiplying, for example, DX holds the high 16 bits of the product.

## Slide 14: Index Registers (SI and DI)
SI and DI stand for source index and destination index respectively
Hold address of data and used in memory access.
For flexibility, Intel allows many mathematical and logical operations on these registers as well like the general registers.
The source and destination are named because of their implied functionality as the source or the destination in a special class of instructions called the string instructions.
SI and DI are 16bit and cannot be used as 8bit register pairs like AX, BX, CX, and DX.

## Slide 15: Instruction Pointer (IP)
This is the special register containing the address of the next instruction to be executed.
No mathematics or memory access can be done through this register.
It is out of our direct control and is automatically used.
Playing with it is dangerous and needs special care.
Program control instructions change the IP register

## Slide 16: Stack Pointer (SP) and Base Pointer (BP)
Stack Pointer (SP) is a memory pointer and is used indirectly by a set of instructions. This register will be explored in the discussion of the system stack.
Base Pointer (BP) It is also a memory pointer containing the address in a special area of memory called the stack and will be explored alongside SP in the discussion of the stack

## Slide 17: Flags Register
The flags register as previously discussed is not meaningful as a unit rather it is bit wise significant and accordingly each bit is named separately. The bits not named are unused. The Intel FLAGS register has its bits organized as follows:
The individual flags are explained in the next table.
Empty positions in figure are undefined.

## Slide 19: Segment Registers (CS, DS, SS, and ES)
The code segment register, data segment register, stack segment register, and the extra segment register are special registers related to the Intel segmented memory model and will be discussed later.

## Slide 20: Bus and Memory
8088 has 8-bit data bus
It has 20 bit address bus
It can access 1MB of memory with this 20 bit address bus
  220 = 1MB

## Slide 21: First Program in Assembly language
The first program that we will write will only add three numbers.
The addition operation is performed on data present in registers.
As addition requires two operands, both the operands should be present in registers (or at least one)
The next slide shows the code with comments.

## Slide 22
Things to note:
  Abbreviations, for example move is written as mov in assembly operation
  Code will always start with Line 2 and
  Code will always ends with Line 9 and 10 to terminate program safely.
  Instructions are written in following format
    operation destination, source
  Code is very much like English language for example
    mov ax,5 means move 5 to ax

## Slide 23: Assemble line and Debug code
NASM (Netwide Assembler)will be used to assemble the code and create executable file with .com extension
AFD (A fullscreen debugger) will be used to debug the code.
DOSBox will be used to emulate 8088 processor.
Installation of these tools will be discussed in lab.
Save the code given in previous slide with .asm extension.
Following command will be used to assemble the code
nasm ex01.asm –o ex01.com –l ex01.lst

## Slide 24: Listing File
The listing file created has a lot of information. Ans is annotated as follow
Offset of instruction in hex
OPCODE in hex and Operand in little-endian hex
Assemble code
Size of last instruction (line 10) is 2 bytes so total size of .com file is 16+2=18bytes
Notes: B8 is to move operand to AX
BB is to move operand to BX
Little-endian is an order in which the "little end" (least significant value in the sequence) is stored first

## Slide 25: Debug
Following command will be used to debug the file
afd ex01.com
The debugger shows the values of registers, flags, stack, our code, and one or two areas of the system memory as data.
Debugger allows us to step our program one instruction at a time and observe its effect on the registers and program data.

## Slide 26
Things to note:
  Registers
  Memory (m1 and m2 view)
  Offset of 1st instruction
  IP
  Hit F1 to execute instruction
  See the change in registers/memory